## Slide 1: Trajectory Planning

## Slide 2: Chapter 5
Trajectory Planning
5.1 INTRODUCTION
Path and trajectory planning relates to the way that a robot is moved from one location to another in a controlled manner.
The sequence of movements for a controlled movement between motion segments, in straight-line motions or in sequential motions.
It requires the use of both kinematics and dynamics of robots.

## Slide 3: 5.1 INTRODUCTION

## Slide 4: Consideration
In order to determine the robot trajectory, consider the location, velocity, position of desired end-effector as well as kinematic constraints condition of robot and dynamic characteristic
kinematic constraints condition : each joint’s range of motion, work space’s limitation, singularity problem
Dynamic characteristic : joint torque’s limitation, maximum velocity, acceleration

## Slide 5: As shown in Fig. 5.A1, the basic problem is to move the manipulator from an initial position to some desired final position.
In general, this motion involves both a change in orientation and a change in position of the tool relative to the station.
FIGURE 5.A1 : In executing a trajectory, a manipulator moves from its initial position to a desired goal position in a smooth manner.

## Slide 6: 5.2 PATH VS. TRAJECTORY
Path: A sequence of robot configurations in a particular order without regard to the timing of these configurations.
Trajectory: It is concerned about when each part of the path must be attained, thus specifying timing.
Fig. 5.1 Sequential robot movements in a path.

## Slide 7: 5.3 JOINT-SPACE VS. CARTESIAN-SPCAE DESCRIPTIONS
Joint-space description:
The description of the motion to be made by the robot by its joint values.
The motion between the two points is unpredictable.
Cartesian space description:
The motion between the two points is known at all times and controllable.
It is easy to visualize the trajectory, but it is difficult to ensure that singularity.
Fig. 5.2 Sequential motions of a robot to follow a straight line.
Fig. 5.3 Cartesian-space trajectory (a) The trajectory specified in Cartesian coordinates may force the robot to run into itself, and (b) the trajectory may requires a sudden change in the joint angles.

## Slide 8: 5.4 BASICS OF TRAJECTORY PLANNING
Let’s consider a simple 2 degree of freedom robot.
We desire to move the robot from Point A to Point B.
Let’s assume that both joints of the robot can move at the maximum rate of 10 degree/sec.
Move the robot from A to B, to run both joints at their maximum angular velocities.
After 2 [sec], the lower link will have finished its motion, while the upper link continues for another 3 [sec].
The path is irregular and the distances traveled by the robot’s end are not uniform.
Fig. 5.4 Joint-space nonnormalized movements of a robot with two degrees of freedom.

## Slide 9: 5.4 BASICS OF TRAJECTORY PLANNING
Fig. 5.5 Joint-space, normalized movements
of a robot with two degrees of freedom.
Both joints move at different speeds, but move continuously together.
The resulting trajectory will be different.
Let’s assume that the motions of both joints are normalized by a common factor such that the joint with smaller motion will move proportionally slower and the both joints will start and stop their motion simultaneously.

## Slide 10: 5.4 BASICS OF TRAJECTORY PLANNING
Fig. 5.6 Cartesian-space movements of a two-degree-of-freedom robot.
Divide the line into five segments and solve for necessary angles  and  at each point.
The joint angles are not uniformly changing.
Let’s assume that the robot’s hand follows a known path between points A and B in a straight line.
The simplest solution would be to draw a line between points A and B, so called interpolation.

## Slide 11: 5.4 BASICS OF TRAJECTORY PLANNING
It is assumed that the robot’s actuators are strong enough to provide large forces necessary to accelerate and decelerate the joints as needed.
Divide the segments differently.
  The arm moves at smaller segments as we speed up at the beginning.
  Go at a constant cruising rate.
  Decelerate with smaller segments as approaching point B.
Fig. 5.7 Trajectory planning with an acceleration-deceleration regiment.
Let’s assume that the robot’s hand follows a known path between point A and B with straight line.
The simplest solution would be to draw a line between points A and B, so called interpolation.

## Slide 12: 5.4 BASICS OF TRAJECTORY PLANNING
Fig. 5.8 Blending of different motion segments in a path.
Next level of trajectory planning is between multiple points for continuous movements.
Stop-and-go motion create jerky motions with unnecessary stops.
Blend the two portions of the motion at point B.
Specify two via point D and E before and after point B
Fig. 5.9 An alternative scheme for ensuring that the robot will go through a specified point during blending of motion segments.
Two via points D and E are picked such that point B will fall on the straight-line section of the segment ensuring that the robot will pass through point B.
E

## Slide 13: Figure 5.A2 shows one possibility where  was chosen quite high. In this case we quickly accelerate, then coast at constant velocity, and then decelerate.
FIGURE 5.A2 : Position, velocity, and acceleration profiles for linear interpolation with parabolic blends. The set of curves on the left are based on a higher acceleration during the blends than is that on the right.

## Slide 14: 5.5 JOINT-SPACE TRAJECTORY PLANNING
5.5.1 Third-Order Polynomial Trajectory Planning
How the motions of a robot can be planned in joint-space with controlled characteristics.
Polynomials of different orders
Linear functions with parabolic blends
The initial location and orientation of the robot is known, and using the inverse kinematic equations, we find the final joint angles for the desired position and
c3t 3
orientation.
 (t)  c0  c1t  c2t 2
 (ti )  i
 (t f )   f
(t )  0
i
(t f )  0
Initial Condition
2
1 2 3
 (t)  c  2c t  3c t

First derivative of the
polynomial of equation
 (ti )  c0  i
f f
 (t f )  c0  c1t f  c2t 2  c3t 3
f
(ti )  c1  0
(t f )  c1  2c2t f  3c3t 2  0
Substituting the initial and final conditions

## Slide 15
  JOINT-SPACE TRAJECTORY PLANNING
5.5.2 Fifth-Order Polynomial Trajectory Planning
    Specify the initial and ending accelerations for a segment.
    To use a fifth-order polynomial for planning a trajectory, the total number of boundary conditions is 6.
Calculation of the coefficients of a fifth-order polynomial with position, velocity and an acceleration boundary conditions can be possible with below equations.
 (t)  c0  c1t  c2t 2  c3t 3  c4t 4  c5t 5
2
1 2 3 4 5
 (t)  c  2c t  3c t  4c t3  5c t 4

 (t)  2c2  6c3t 12c4t 2  20c5t 3

## Slide 16: 5.5 JOINT-SPACE TRAJECTORY PLANNING
Linear segment can be blended with parabolic sections at the beginning and the end of the motion segment, creating continuous position and velocity.
Acceleration is constant for the parabolic sections, yielding a continuous velocity at the common points A and B.
Fig. 5.13 Scheme for linear segments with parabolic blends.
2
 (t)  c0  c1t  1 c2t 2
(t)  c1  c2t
 (t)  c2
2
 (t)  i  1 c2t 2
2
(t)  c t
 (t)  c2
2nd
1st
2nd

## Slide 17: 5.5 JOINT-SPACE TRAJECTORY PLANNING
Initial velocity 0, a constant known joint velocity  in the linear portion, final velocity 0
1
 (t  0)  i  c0
(t  0)  0  c
 (t)  c2
1
c0  i
c  0

 2
c  
2
2
2
1
2
f
f b
i
i 2 b
f
b
i
b
f
b
tb
t

c  
  B  A i   2A  (t  2t ) 
 2 
 2 i  c2tb   (t f  2tb ) i


   c t  (t
 2t )


  
t  (t
 2t )
 
 b 
i  f  t f

tb 
2
1
2
A i 2 b
    c t
A
2 b
  c t  
f
B
A
f
A
b
B
A

 
    ((t  tb )  tb ))    (t  2t )
 
 
A
f
2 b
 0
  c t  
Constant joint velocity

## Slide 18: 5.5 JOINT-SPACE TRAJECTORY PLANNING
Linear function with parabolic blends for a path with via points
Figure 1.9 shows a set of joint-space via points for
some joint .
FIGURE 1.9 : Multisegment linear path with blends


## Slide 19: 5.5 JOINT-SPACE TRAJECTORY PLANNING
5.5.4 Linear Segments with Parabolic Blends and Via Points
The position of the robot at time t0 is known and using the inverse kinematic equations of the robot, the joint angles at via points and at the end of the motion can be found.
To blend the motion segments together, the boundary conditions of each point to calculate the coefficients of the parabolic segments is used.
Maximum allowable accelerations should not be exceeded.

## Slide 20: 5.5 JOINT-SPACE TRAJECTORY PLANNING
Combinations of lower order polynomials for different segments of the trajectory and blending together to satisfy all required boundary conditions is required.
5.5.5 Higher Order Trajectories
Incorporating the initial and final boundary conditions together with this information enables us to use higher order polynomials in the below form, so that the trajectory will pass through all specified points.
 (t)  c0  c1t  c2t 2  c3t 3  cn1t n1  cntn
It requires extensive calculation for each joint and higher order polynomials.
3-5-3 trajectory
4-3-4 trajectory

## Slide 21: 5.6 CARTESIAN-SPACE TRAJECTORIES
Cartesian-space trajectories relate to the motions of a robot relative to the Cartesian reference frame.
In Cartesian-space, the joint values must be repeatedly calculated through the inverse kinematic equations of the robot.
Computer Loop Algorithm
Increment the time by t=t+Dt.
Calculate the position and orientation of the hand based on the selected function for the trajectory.
Calculate the joint values for the position and orientation through the inverse kinematic equations of the robot.
Send the joint information to the controller.
Go to the beginning of the loop

## Slide 22: 5.6 CARTESIAN-SPACE TRAJECTORIES
If possible, we still prefer to plan Cartesian trajectories
separately for position and orientation
The number of knots to be interpolated in the Cartesian space is
typically low (e.g., 2 knots for a PTP motion, 3 if a “via point” is added): use simple interpolating paths, such as straight lines…

## Slide 23
L
pi
pf
path parameterization
i
f
i
p(s)  p  s( p  p )
GIVEN
pi , p f , vmax , amax
vi , v f (typically = 0)
L= p f  pi
p f  pi
p f  pi
unit vector of line
= direction cosines
  CARTESIAN-SPACE TRAJECTORIES
    Planning a linear Cartesian path(position only)

## Slide 24
s [0,1]
setting s = σ/L, σ ∈ [0,L] is the arc length (gives the current length of the path)
f i
ds
L
p (s)  dp s  ( p  p )s
 p f  pi 
2
f
i
d 2 p dp
ds2 ds
L
p(s) 

s  s  ( p
 p )s
 p f  pi 
  CARTESIAN-SPACE TRAJECTORIES
    Planning a linear Cartesian path(position only)
p(s)  pi  s( p f  pi )

## Slide 25
given* : L, vmax, amax
find : Ts , T
max
s
V (T  T )  L
= area of the Speed profile
max
s
a
L
vmax
T 
T  vmax
Lamax  vmax 2
amax vmax
 T  T s 
a □"coast"□phase exists iff: L > vmax 2 / amax
* = other input data combinations are possible (see textbook)
5.6 CARTESIAN-SPACE TRAJECTORIES
Timing law with trapezoidal speed -1

## Slide 26
max
max
max
2
2
max
max
max s
s
s
s
a t 2 / 2
vmax 2
2a
v
max
amax
t [0,T ]




v t 
t [Ts ,T  Ts ]

a (t  T )
 (t)   
vmax d  vmax  c
t [T-T ,T ]
/2  v T 
c  a T 2 / 2,
  t  T









can be used also in the joint space!
  CARTESIAN-SPACE TRAJECTORIES
    Timing law with trapezoidal speed -2
v
amax
Ts  max

## Slide 27
z B =“via point”
C’
A’ over-fly
A
x
AB
B  A  K
B  A
C  B
 KBC
C  B
unit vectors of direction cosines
on linear path AB
on linear path BC
1
given: constant speeds v
v2
desired transition: with constant acceleration for a time T
 x(t) 
p(t)   y(t)  t [0, T ](transition starts at t = 0)
 
 z(t) 
 
note: during over-fly, the path remains always in the plane specified by the two lines intersecting at B (in essence, it is a planar problem)
  CARTESIAN-SPACE TRAJECTORIES
    Concatenation of linear paths
C

## Slide 28: 5.6 CARTESIAN-SPACE TRAJECTORIES
Time profiles on components

## Slide 29
z B
A’
A
x
C’
C
y
AB
B  A  K
B  A
C  B
 KBC
C  B
unit vectors of direction cosines
 x(t) 
p(t)   y(t) 
t [0, T ](transition starts at t = 0)
 
 z(t) 
 
p(t)  (1/ T )(v2 KBC  v1K AB )
p (t)  v1K AB  (t / T )(v2 KBC  v1K AB )
p(t)  A ' v1K ABt  (t 2 / 2T )(v2 KBC  v1K AB )


thus, we obtain a parabolic blending
(see textbook for this same
approach in the joint space)
  CARTESIAN-SPACE TRAJECTORIES
    Timing law during transition

## Slide 30
z
A’
A
x
C’
C
y
d1
B d2
B  A'  d1KAB
C'  B  d2 KBC
①
p(t)  A'  v1K ABt  (t 2 / 2T )(v2 KBC  v1K AB )
p(T )  A'  (T / 2)(v1K AB  v2 KBC )  C'
 B  A' + (T / 2)(v1K AB  v2 KBC )  C'  B
d1KAB  d2 KBC  (T / 2)(v1K AB  v2 KBC )
1
d1  v1T / 2
d2  v2T / 2
by choosing, e.g., d1
(namely A' )
T  2d1 / v1
d2  d1v2 / v1
  CARTESIAN-SPACE TRAJECTORIES
    Solution(various options)

## Slide 31
A
similarly)
ΔT=4
d2 =3
5.6 CARTESIAN-SPACE TRAJECTORIES
A numerical example
  transition from A=(3,3) to C=(8,9) via B=(1,9), with speed from v1 =1 tov2 =2
  exploiting two options for solution (resulting in different paths!)
    assign transition time: ΔT=4 (actually, re-centered for t ∈ [-ΔT/2, ΔT/2])
    assign distance from B for departing: d2 =3 (assign d2 for landing is handled

## Slide 32: 5.6 CARTESIAN-SPACE TRAJECTORIES
A numerical example(cont’d)
  first option: ΔT=4 (resulting in d1 =2, d2 =4)

## Slide 33: 5.6 CARTESIAN-SPACE TRAJECTORIES
A numerical example(cont’d)
  first option: ΔT=4 (resulting in d1 =2, d2 =4)

## Slide 34: 5.6 CARTESIAN-SPACE TRAJECTORIES
A numerical example(cont’d)
  second option: d1 =3 (resulting in ΔT=6, d2 =6)

## Slide 35: 5.6 CARTESIAN-SPACE TRAJECTORIES
actually, the same vel/acc profiles only with a different time scale
A numerical example(cont’d)
  second option: d1 =3 (resulting in ΔT=6, d2 =6)

## Slide 36
A
B
C'
B
A'
..
p(t)  (1/ T )(v2 KBC  v1K AB )
..
v1  v2  vmax ( for simplicity)
p(t)  amax
Kbc, y K AB, y  KBC , z K AB, z )
T  (vmax / amax ) KBC  K AB
 (vmax / amax ) 2(1 KBC , x K AB, x
then, d1  d2  vmax T /2
5.6 CARTESIAN-SPACE TRAJECTORIES
Alternative solution
  imposing acceleration

## Slide 37
that avoids the obstacle O, with
a  amax and v  vmax
O
B
C
¨
C
¨
C
A' A¨
B
Add a via point B “sufficiently far” from O
on AA '  amax ; on A ' B and BC '  vmax on C 'C  amax'
over  flybetween A '' e C '';
5.6 CARTESIAN-SPACE TRAJECTORIES
Application example
plan a Cartesian trajectory from A to C (rest-to-rest)

## Slide 38: 5.6 CARTESIAN-SPACE TRAJECTORIES
Actual manipulator operates by joint coordinates. Beforehand we have to decide to represent trajectory as Cartesian coordinates or Joint coordinates.
It can be expressed in the following 3 ways.

## Slide 39: 5.6 CARTESIAN-SPACE TRAJECTORIES
Method 1
Within each sampling period, conversion of Cartesian coordinates and joint coordinates
To calculate the error between desired path and actual path, current location points are converted to the corresponding points on the Cartesian coordinates by using the Jacobian transformation.
Errors of joint space use inverse Jacobian.
Disadvantages : Calculation is complicated. Therefore, controller’s sampling frequency is limited.

## Slide 40: 5.6 CARTESIAN-SPACE TRAJECTORIES
Method 2
The trajectory displayed at the joint coordinate system.
The constraints on the manipulator’s maximum permissible speed and acceleration is considered. These constraints is displayed at the reference coordinate system or the generalized coordination of joint space. The path notation that is placed on another space can represent the relationship, using the kinematic equations.

## Slide 41: 5.6 CARTESIAN-SPACE TRAJECTORIES
Method 3
The function, such as the polynomial, is used to represent the path that connect the two adjacent trajectories in the joint space.
These function can control manipulator to be flexible and be adjusted to meet the consecutive conditions.

## Slide 42: 5.7 DESCRIPTION OF PATHS WITH A ROBOT PROGRAMMING LANGUAGE
We will illustrate how various types of paths that we have discussed in this chapter might be specified in a robot language.
In these examples, we use the syntax of AL, a robot programming language developed at Stanford University.

## Slide 43: 5.7 DESCRIPTION OF PATHS WITH A ROBOT PROGRAMMING LANGUAGE
The symbols A, B, C, and D stand for variables of type "frame" in the AL-language examples below. These frames specify path points
that we will assume have been taught or textually described to the system. Assume that the manipulator begins in position A.
To move the manipulator in joint-space mode along linear- parabolic-blend paths, we could say
move ARM to C with duration = 3*seconds;

## Slide 44: 5.7 DESCRIPTION OF PATHS WITH A ROBOT PROGRAMMING LANGUAGE
To move to the same position and orientation in a straight line we could say
move ARM to C linearly with duration = 3*seconds;
where the clause "linearly" denotes that Cartesian straight-line motion
is to be used. If duration is not important, the user can omit this specification, and the system will use a default velocity- that is,
move ARM to C;

## Slide 45: 5.7 DESCRIPTION OF PATHS WITH A ROBOT PROGRAMMING LANGUAGE
A via point can be added, and we can write
move ARM to C via B;
or a whole set of via points might be specified by
move ARM to C via B,A,D;
Note that in
move ARM to C via B with duration = 6*seconds; the duration is given for the entire motion.

## Slide 46: 5.7 DESCRIPTION OF PATHS WITH A ROBOT PROGRAMMING LANGUAGE
The system decides how to split this duration
between the two
segments. It is possible in AL to specify the duration of a single segment- for example, by
move ARM to C via B where duration = 3*seconds;
The first segment which leads to point B will have a duration of 3 seconds.

## Slide 47: 5.8 PLANNING PATHS WHEN USING THE DYNAMIC MODEL
Usually, when paths are planned, we use a default or a maximum acceleration at each blend point. Actually, the amount of acceleration that the manipulator is capable of at any instant is a function of the dynamics of the arm and the actuator limits.
Most actuators are not characterized by a fixed maximum torque or acceleration, but rather by a torque-speed curve.

## Slide 48: 5.8 PLANNING PATHS WHEN USING THE DYNAMIC MODEL
When we plan a path assuming there is a maximum acceleration at each joint or along each degree of freedom, we are making a tremendous simplification. In order to be careful not to exceed the actual capabilities of the device, this maximum acceleration must be chosen conservatively.
We might ask the following question: Given a desired spatial path of the end-effector, find the timing information (which turns a description of a spatial path into a trajectory) such that the manipulator reaches the goal point in minimum time. Such problems have been solved by numerical means. The solution takes the rigid body dynamics into account as well as actuator speed-torque constraint curves.