## Slide 1: Measuring Instruments
Electrical Measurement

## Slide 2: Classification of Measuring
Instruments
Electrical instruments may be divided into two categories, that are;
Absolute instruments,
Secondary instruments.

## Slide 3: Absolute instruments
🞇 Absolute instruments or Primary Instruments:- These instruments gives the magnitude of quantity under measurement in terms of physical constants of the instrument e.g. Tangent Galvanometer. These instruments do not require comparison with any other standard instrument
🞇 • These instruments give the value of the electrical quantity in terms of absolute quantities (or some constants) of the instruments and their deflections.
In this type of instruments no calibration or comparison with other instruments is necessary.
They are generally not used in laboratories and are seldom used in practice by electricians and engineers. They are mostly used as means of standard measurements and are maintained by national laboratories and similar institutions.

## Slide 4
Some of the examples of absolute instruments are:
Tangent galvanometer
Raleigh current balance
Absolute electrometer

## Slide 5: Secondary instruments
🞇 In Secondary instruments the deflection gives the magnitude of electrical quantity to be measured directly. These instruments are required to be calibrated by comparing with another standard instrument before putting into use.

## Slide 6: Secondary Instruments
1.Recording instrument
This type of instruments records the magnitude of the quantity to be measured continuously over specified period of time.
3. Integrating instrument
This type of instrument gives the total amount of the quantity to be measured over a specified period of time.

## Slide 7: Secondary Instruments
3. Indicating instrument
This instrument uses a dial and pointer to determine the value of measuring quantity. The pointer indication gives the magnitude of measuring quantity
4. Electromechanical indicating instrument
For satisfactory operation electromechanical indicating instrument, three forces are necessary They are
(a) Deflecting force (b) Controlling force
(c)Damping force

## Slide 8: Basic Secondary instruments
which we use
Multi meter
Clamp meter
Ammeter
Voltmeter
Wartmeter

## Slide 9
Measuring current, voltage, and resistance
A
Ammeter:
measures current (A)
connected in series
(current must go through instrument)
I
V
a
b
Voltmeter:
measures potential difference (V)
connected in parallel
Ohmmeter:
measures resistance of an isolated resistor (not in a working circuit)


## Slide 10
Effect of ammeter on circuit
V
R
Measuring current in a simple circuit:
A
connect ammeter in series
Are we measuring the correct current?
(the current in the circuit without ammeter)

## Slide 11
current without the ammeter would be
V
R
Measuring current in a simple circuit:
To minimize error, ammeter resistance r must be very small.
(ideal ammeter would have zero resistance)
any ammeter has some resistance r.
r
connect ammeter in series
Are we measuring the correct current?
(the current in the circuit without ammeter)
current in presence of ammeter is
Effect of ammeter on circuit

## Slide 12
Example: an ammeter of resistance 10 m is used to measure the current through a 10  resistor in series with a 3 V battery that has an internal resistance of 0.5 . What is the relative (percent) error caused by the ammeter?
V=3 V
R=10 
r=0.5 
Actual current without ammeter:
You might see the symbol  used instead of V.

## Slide 13
V=3 V
R=10 
r=0.5 
Current with ammeter:
RA

## Slide 14
Designing an ammeter
http://hyperphysics.phy-astr.gsu.edu/hbase/magnetic/galvan.html#c1
Galvanometer:
current flows through a coil in a magnetic field
coil experiences a torque, connected needle deflects
(see later chapters of this class)

## Slide 15
Designing an ammeter
ammeter can be based on galvanometer
(for electronic instrument, use electronic sensor instead, analysis still applies)
simplest case: send current directly through galvanometer, observe deflection of needle
Needle deflection is proportional to current. Each galvanometer has a certain maximum current corresponding to full needle deflection.
What if you need to measure a larger current?
use shunt resistor

## Slide 16
Ammeter uses a galvanometer and a shunt, connected in parallel:
A
I

Everything inside the green box is the ammeter.
Current I gets split into Ishunt and IG
Homework hint:
If your galvanometer reads 1A full scale but you want the ammeter to read 5A full scale, then RSHUNT must result in IG=1A when I=5A. What are ISHUNT and VSHUNT?
G
RG
RSHUNT
IG
ISHUNT
I
A
B
galvanometer

## Slide 17
G
RG
RSHUNT
IG
ISHUNT
I
A
B
Shunt also reduces resistance of the ammeter:

## Slide 18
A galvanometer-based ammeter uses a galvanometer and a shunt, connected in parallel:
G
RG
RS
IG
IS
I
Example: what shunt resistance is required for an ammeter to have a resistance of 10 m, if the galvanometer resistance is 60 ?
(actually 0.010002 )
To achieve such a small resistance, the shunt is probably a large-diameter wire or solid piece of metal.

## Slide 19
Effect of voltmeter on circuit
Measuring voltage (potential difference) Vab in a simple circuit:
connect voltmeter in parallel
Are we measuring the correct voltage?
(the voltage in the circuit without voltmeter)
=3 V
R=10 
r=0.5 
V
a
b

## Slide 20
extra current changes voltage drop across r and thus Vab
To minimize error, voltmeter resistance r must be very large.
(ideal voltmeter would have infinite resistance)
voltmeter has some resistance RV
current IV flows through voltmeter
Effect of voltmeter on circuit
Measuring voltage (potential difference) Vab in a simple circuit:
connect voltmeter in parallel
Are we measuring the correct voltage?
(the voltage in the circuit without voltmeter)
=3 V
R=10 
r=0.5 
RV
a
b
IV

## Slide 21
Example: a galvanometer of resistance 60  is used to measure the voltage drop across a 10 k resistor in series with an ideal 6 V battery and a 5 k resistor. What is the relative error caused by the nonzero resistance of the galvanometer?
Actual voltage drop without instrument:
V=6 V
R1=10 k
R2=5 k
a
b

## Slide 22
The measurement is made with the galvanometer.
V=6 V
R1=10 k
R2=5 k
G
RG=60 
a
b
60  and 10 k resistors in parallel are equivalent to 59.6  resistor.
Total equivalent resistance: 5059.6 
Total current: I=1.186x10-3 A
I=1.19 mA
Vab = 6V – IR2 = 0.07 V.
The relative error is:
Would you pay for this voltmeter?
Would you pay for this voltmeter?
We need a better instrument!

## Slide 23
Example: a voltmeter of resistance 100 k is used to measure the voltage drop across a 10 k resistor in series with an ideal 6 V battery and a 5 k resistor. What is the percent error caused by the nonzero resistance of the voltmeter?
We already calculated the actual voltage drop (2 slides back).
V=6 V
R1=10 k
R2=5 k
a
b

## Slide 24
The measurement is now made with the “better” voltmeter.
V=6 V
R1=10 k
R2=5 k
V
RV=100 k
a
b
100 k and 10 k resistors in parallel are equivalent to an 9090  resistor.
Total equivalent resistance: 14090 
Total current: I=4.26x10-4 A
I=.426 mA
The voltage drop from a to b:
6-(4.26x10-4)(5000)=3.87 V.
The percent error is.
Not great, but much better.

## Slide 25
voltmeter must have a very large resistance
voltmeter can be made from galvanometer in series with a large resistance
V
G
RG
RSer

Everything inside the blue box is the voltmeter.
a
b
Vab
a
b
Vab
Homework hints: “the galvanometer reads 1A full scale” would mean a current of IG=1A would produce a full-scale deflection of the galvanometer needle.
If you want the voltmeter shown to read 10V full scale, then the selected RSer must result in IG=1A when Vab=10V.
Homework hints: “the galvanometer reads 1A full scale” would mean a current of IG=1A would produce a full-scale deflection of the galvanometer needle.
If you want the voltmeter shown to read 10V full scale, then the selected RSer must result in IG=1A when Vab=10V.
Designing a voltmeter

## Slide 26
Example:
It s desired to measure the voltage across a 50 kΩ resistor in the circuit shown In Fig.Two voltmeters are available for this purpose :
Voltmeter A with a sensitivity of 1000Ω/V and
Voltmeter B with a sensitivity of 20,000 Ω/V.
Both meters have 0-50 V range. Calculate:
(a) the reading of each voltmeter ;
(b) the error in each reading expressed as a percentage
of true value.

## Slide 27
Ohmmeter measures resistance of isolated resistor
Ohmmeter can be made from a galvanometer, a series resistance, and a battery (active device).
G
RG
RSer
R=?
Terminals of ohmmeter are connected to unknown resistor
battery causes current to flow and galvanometer to deflect
V=I (Rser + RG + R) solve for unknown R

Measuring Instruments: Ohmmeter
Everything inside the blue box is the ohmmeter.
V

## Slide 28
Alternatively:
separately measure current and voltage for resistor
Apply Ohm’s law
Four-point probe:
V
A
reference: http://hyperphysics.phy-astr.gsu.edu/hbase/magnetic/movcoil.html#c4