## Slide 1: CSE4421/5324: Introduction to Robotics
From:Thrun, Burgard and Fox, Probabilistic Robotics, The MIT Press, 2006, CSEB 1012J, burton@cse.yorku.ca

## Slide 2: A150 Robotic Arm
link 3
link 2

## Slide 3: Kinematics
the study of motion that ignores the forces that cause the motion
  “geometry of motion”
interested in position, velocity, acceleration, etc. of the various links of the manipulator
  e.g., where is the gripper relative to the base of the manipulator? what direction is it pointing in?
  described using rigid transformations of the links

## Slide 4: Kinematics
forward kinematics:
  given the link lengths and joint angles compute the position and orientation of the gripper relative to the base
    for a serial manipulator there is only one solution
inverse kinematics:
  given the position (and possibly the orientation) of the gripper and the dimensions of the links, what are the joint variables?
    for a serial manipulator there is often more than one mathematical solution

## Slide 5: Wheeled Mobile Robots
robot can have one or more wheels that can provide
  steering (directional control)
  power (exert a force against the ground)
an ideal wheel is
  perfectly round (perimeter 2πr)
  moves in the direction perpendicular to its axis

## Slide 6: Wheel

## Slide 7: Deviations from Ideal

## Slide 8: Differential Drive
two independently driven wheels mounted on a common axis

## Slide 9: Forward Kinematics
for a robot starting with pose [0 0 0]T moving with velocity V(t) in a direction θ(t) :

## Slide 10: Sensitivity to Wheel Velocity
σ = 0.05
σ = 0.01

## Slide 11: Localization using Landmarks: RoboSoccer

## Slide 12: Maps
 |  |  |  |  |  |  |  |  |  |  |  |  |  |  | *
* |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
start
goal

## Slide 13: Path Finding
start
goal

## Slide 14: Localization
start
goal

## Slide 15: EKF SLAM Application
[MIT B21, courtesy by John Leonard]
www.probabilistic-robotics.org

## Slide 16: EKF SLAM Application
raw odometry
estimated trajectory
[courtesy by John Leonard]
www.probabilistic-robotics.org

## Slide 17
Introduction to manipulator kinematics

## Slide 18: Robotic Manipulators
a robotic manipulator is a kinematic chain
  i.e. an assembly of pairs of rigid bodies that can move respect to one another via a mechanical constraint
the rigid bodies are called links
the mechanical constraints are called joints

## Slide 19: A150 Robotic Arm
link 3
link 2

## Slide 20: Joints
most manipulator joints are one of two types
revolute (or rotary)
  like a hinge
  allows relative rotation about a fixed axis between two links
    axis of rotation is the z axis by convention
prismatic (or linear)
  like a piston
  allows relative translation along a fixed axis between two links
    axis of translation is the z axis by convention
our convention: joint i connects link i – 1 to link i
  when joint i is actuated, link i moves

## Slide 21: Joint Variables
revolute and prismatic joints are one degree of freedom (DOF) joints; thus, they can be described using a single numeric value called a joint variable
qi : joint variable for joint i
revolute
  qi = qi : angle of rotation of link i relative to link i – 1
prismatic
  qi = di : displacement of link i relative to link i – 1

## Slide 22: Revolute Joint Variable
revolute
  qi = qi : angle of rotation of link i relative to link i – 1
link i – 1
link i
qi

## Slide 23: Prismatic Joint Variable
prismatic
  qi = di : displacement of link i relative to link i – 1
link i – 1
link i
di

## Slide 24: Common Manipulator Arrangments
most industrial manipulators have six or fewer joints
  the first three joints are the arm
  the remaining joints are the wrist
it is common to describe such manipulators using the joints of the arm
  R: revolute joint
  P: prismatic joint

## Slide 25: Articulated Manipulator
RRR (first three joints are all revolute)
joint axes
  z0 : waist
  z1 : shoulder (perpendicular to z0)
  z2 : elbow (parallel to z1)
z0
z1
z2
waist
shoulder
elbow
forearm
q1
q2
q3

## Slide 26: Spherical Manipulator
RRP
Stanford arm
  http://infolab.stanford.edu/pub/voy/museum/pictures/display/robots/IMG_2404ArmFrontPeekingOut.JPG
z0
z1
z2
waist
shoulder
q1
q2
d3

## Slide 27: SCARA Manipulator
RRP
Selective Compliant Articulated Robot for Assembly
  http://www.robots.epson.com/products/g-series.htm
z0
z1
z2
q1
q2
d3

## Slide 28: Forward Kinematics
given the joint variables and dimensions of the links what is the position and orientation of the end effector?
q2
q1
a1
a2

## Slide 29: Forward Kinematics
choose the base coordinate frame of the robot
  we want (x, y) to be expressed in this frame
q2
q1
a1
a2
(x, y) ?
x0
y0

## Slide 30: Forward Kinematics
notice that link 1 moves in a circle centered on the base frame origin
q2
q1
a1
a2
(x, y) ?
x0
y0
( a1 cos q1 , a1 sin q1 )

## Slide 31: Forward Kinematics
choose a coordinate frame with origin located on joint 2 with the same orientation as the base frame
q2
q1
a1
a2
(x, y) ?
x0
y0
( a1 cos q1 , a1 sin q1 )
q1
x1
y1

## Slide 32: Forward Kinematics
notice that link 2 moves in a circle centered on frame 1
q2
q1
a1
a2
(x, y) ?
x0
y0
( a1 cos q1 , a1 sin q1 )
q1
x1
y1
( a2 cos (q1 + q2),
a2 sin (q1 + q2) )

## Slide 33: Forward Kinematics
because the base frame and frame 1 have the same orientation, we can sum the coordinates to find the position of the end effector in the base frame
q2
q1
a1
a2
x0
y0
( a1 cos q1 , a1 sin q1 )
q1
x1
y1
( a2 cos (q1 + q2),
a2 sin (q1 + q2) )
(a1 cos q1 + a2 cos (q1 + q2),
a1 sin q1 + a2 sin (q1 + q2) )

## Slide 34: Forward Kinematics
we also want the orientation of frame 2 with respect to the base frame
  x2 and y2 expressed in terms of x0 and y0
q2
q1
a1
a2
x0
y0
q1
x2
y2

## Slide 35: Forward Kinematics
without proof I claim:
q2
q1
a1
a2
x0
y0
q1
x2 = (cos (q1 + q2),
sin (q1 + q2) )
y2 = (-sin (q1 + q2),
cos (q1 + q2) )
x2
y2

## Slide 36: Inverse Kinematics
given the position (and possibly the orientation) of the end effector, and the dimensions of the links, what are the joint variables?
q2 ?
q1 ?
a1
a2
x0
y0
x2
y2
(x, y)

## Slide 37: Inverse Kinematics
harder than forward kinematics because there is often more than one possible solution
a1
a2
x0
y0
(x, y)

## Slide 38: Inverse Kinematics
law of cosines
q2 ?
a1
a2
x0
y0
(x, y)
b

## Slide 39: Inverse Kinematics
and we have the trigonometric identity
therefore,
We could take the inverse cosine, but this gives only one of the two solutions.

## Slide 40: Inverse Kinematics
to obtain
Instead, use the two trigonometric identities:
which yields both solutions for q2 . In many programming languages you would use the
four quadrant inverse tangent function atan2
c2 = (x*x + y*y – a1*a1 – a2*a2) / (2*a1*a2);
s2 = sqrt(1 – c2*c2);
theta21 = atan2(s2, c2);
theta22 = atan2(-s2, c2);

## Slide 41: Inverse Kinematics
Exercise for the student: show that